## Slide 1
◎ Power board troubleshooting
◎ Power troubleshooting
◎ Display troubleshooting
◎ Audio troubleshooting
◎ Function troubleshooting
TPD.SK632.PC821
Trouble Shooting
Author: Checked By: Approved By:

## Slide 2
1. Power Board Diagram
AC
input
EMI
filter
Rectifie
DC/DC
Power convertor
Output
filter
Output
filter
Output
filter
DC/DC
Power convertor
PFC
Feed
back
380VDC output
12V
output
380VDC output
Feed
back
Feed
back
LED
output
LED
power amplifier、
The main IC、
Screen voltage
and so on
BL_ON PWM_REF

## Slide 3
Check EMI open
or L N short,
QB201 short
Check if FB1 Open
Check the power
components
damage or not
Check the rectifier
Check if output short
Check if RB101,
RB102 open
Non output, IR indicator light slake
Check if 12V output normal
Check if EB201 voltage
about 380VDC
Check if UB101 PIN5
voltage is about 15V
Change damaged
components
Change short
components
Change damage resistors
Change UB101
2. Power Supply Trouble 1
N
Y
Y
Y
Y
Y
Y
Y
N
N
N
N
N
Check if EB201 voltage
about 380VDC
See next page

## Slide 4
3. Power Supply Trouble 2
Y
Check if EB201
voltage about
380VDC
Y
Check if
UB202 PIN6
voltage is
about12V
Y
N
N
Y
Check if BL_ON Control signal
Change damage resistors
Check if UB202&UB202 PIN1 components
damage or not
Change damaged
components
Y
Check if
RB210&QB304 &PCB303 &QB305 components
damage
Go to check
Main board
function
N
Y
IR indicator light
up but backlight slake

## Slide 5
Correct
the LED
cable
Check PWM_REF&
BL_ON Control signal
Check
Main
board
function
Change DB304
Check if LED output short/open
IR indicator light
up but backlight slake
Check if the LED output cable are
connected incorrectly or open
Check DB04
damage or not
Remove short/open status
4. Power supply for LED drive
Y
N
Y
Y
Y
Y
Y
N
N
Increase brightness/check if Sampling resistor is right
Y
check is part of the brightness is in dim status
check is all of the brightness is in dim status
Check if UB301 PIN5 voltage is about 15V
N
Change UB301

## Slide 6
一. power
Check if CD12 is 12V
Check power function
Check test points: 5V-STB、3V3_STB、1V5_DDR voltage is normal
Power on, check whether QM1 has 5V_M, and check whether the voltages of VDDC_0.97V, CPU_1V02, 3.3V_M, 1.8_EMMC,2V5_M are normal
Y
N
N
Y
Modify the corresponding circuit:
5V_STB—Check the UD1 module power
3V3_STB--- Check UD2 circuit
1V5_DDR—Check UD6 circuit.
Y
OK
Modify the corresponding circuit:
3.3V_M—Check QM2 circuit
1.8_EMMC—Check UL11 circuit
VDDC_0.97V—Check UD4 circuit
CPU_1V02—Check UD3 circuit
2V5_M—Check UD5 circuit
N

## Slide 7
二. Display (fancy screen)
fancy screen
Check whether the screen cable matches
and whether the connection is firm
Check whether the screen is normal
Change the screen line, reconnect
the screen line
Y
N
Screen change
N
Y
Check between the main chip and the
V-by-one socket
Is the circuit normal
Y
N
Incorrect software or
damaged main chip
Modify this part of the circuit

## Slide 8
三. Display (white screen)
Blank screen
Check whether the screen
voltage is normal
N
Y
Check QW1, QW2 circuit
Check whether the main chip
has video signal output
Change screen or change
screen line
Replace the main IC chip
Y
N

## Slide 9
四. Black screen
Black screen
Check whether the backlight
power supply is normal
Check if the backlight bar
is damaged
N
N
Y
Y
Replace the main IC U1 chip
Check the backlight circuit
Check whether the BL_ON signal
is normal
Y
Replace the backlight strip

## Slide 10
五. Audio (no sound)
no sound
Check whether the power supply of the
power amplifier is normal:
Check the external power board
Check if the voltage of MUTE pin
is normal
Check the MUTE pin control circuit
Check whether the audio input of the
power amplifier is normal
Check whether the circuit between
the power amplifier and the speaker
socket is normal
Check whether the audio output of
the power amplifier is normal
Check the circuit between the main
chip and the power amplifier
Replace the power amplifier chip
N
Y
N
N
N
Y
Y
Y

## Slide 11
六. Function (TV)
Can't find station
Check whether the RF
signal input is normal
Replace the RF signal source
Check if the tuner power
supply is normal
Check the power supply circuit
Check if IIC is working properly
Correct IIC circuit abnormality
Check if the tuner has an
intermediate frequency signal output
Check Tuner and surrounding circuits
Replace the main IC chip
N
Y
N
N
N
Y
Y
Y

## Slide 12
七. Function (USB)）
U disk is not recognized
Check whether the power supply
at the terminal is normal
Check the USB switch circuit
Check whether the main chip pin
signal is normal
Check the circuit between the
terminal and the main chip
main chip is damaged
N
Y
N
Y

## Slide 13
八、Function (HDMI, CVBS)
CI card is not recognized
Check whether the power supply
of the CI card is normal
Check external signal source
Check whether the main chip pin
signal is normal
Check the circuit between the terminal
and the main chip
main chip is damaged
N
Y
N
Y

## Slide 14
九. Function (CI)
CI
Check whether the terminal
power supply is normal
Check the 5V_M circuit
Check whether the DETECT
level is normal
Troubleshoot the DETECT circuit
main chip is damaged
N
Y
N
Y