## Slide 1
◎ Power board troubleshooting
◎ Power troubleshooting
◎ Display troubleshooting
◎ Audio troubleshooting
◎ Function troubleshooting
TPD.SK332.PB801
Trouble Shooting
Author: Checked By: Approved By:

## Slide 2
一. power
Check if CD12 is 12V
Check power function
Check test points: 5V-STB、3V3_STB、1V5_DDR voltage is normal
Power on, check whether QM1 has 5V_M, and check whether the voltages of VDDC_0.97V, CPU_1V02, 3.3V_M, 1.8_EMMC,2V5_M are normal
Y
N
N
Y
Modify the corresponding circuit:
5V_STB—Check the UD1 module power
3V3_STB--- Check UD2 circuit
1V5_DDR—Check UD4 circuit.
Y
OK
Modify the corresponding circuit:
3.3V_M—Check QM2 circuit
1.8_EMMC—Check UL11 circuit
VDDC_0.97V—Check UD4 circuit
CPU_1V02—Check UD3 circuit
2V5_M—Check UD5 circuit
N

## Slide 3
二. Display (fancy screen)
fancy screen
Check whether the screen cable matches
and whether the connection is firm
Check whether the screen is normal
Change the screen line, reconnect
the screen line
Y
N
Screen change
N
Y
Check between the main chip and the
V-by-one socket
Is the circuit normal
Y
N
Incorrect software or
damaged main chip
Modify this part of the circuit

## Slide 4
三. Display (white screen)
Blank screen
Check whether the screen
voltage is normal
N
Y
Check QW1, QW2 circuit
Check whether the main chip
has video signal output
Change screen or change
screen line
Replace the main IC chip
Y
N

## Slide 5
四. Black screen
Black screen
Check whether the backlight
power supply is normal
Check if the backlight bar
is damaged
N
N
Y
Y
Replace the main IC U1 chip
Check the backlight circuit
Check whether the BL_ON signal
is normal
Y
Replace the backlight strip

## Slide 6
五. Audio (no sound)
no sound
Check whether the power supply of the
power amplifier is normal:
Check the external power board
Check if the voltage of MUTE pin
is normal
Check the MUTE pin control circuit
Check whether the audio input of the
power amplifier is normal
Check whether the circuit between
the power amplifier and the speaker
socket is normal
Check whether the audio output of
the power amplifier is normal
Check the circuit between the main
chip and the power amplifier
Replace the power amplifier chip
N
Y
N
N
N
Y
Y
Y

## Slide 7
六. Function (TV)
Can't find station
Check whether the RF
signal input is normal
Replace the RF signal source
Check if the tuner power
supply is normal
Check the power supply circuit
Check if IIC is working properly
Correct IIC circuit abnormality
Check if the tuner has an
intermediate frequency signal output
Check Tuner and surrounding circuits
Replace the main IC chip
N
Y
N
N
N
Y
Y
Y

## Slide 8
七. Function (USB)）
U disk is not recognized
Check whether the power supply
at the terminal is normal
Check the USB switch circuit
Check whether the main chip pin
signal is normal
Check the circuit between the
terminal and the main chip
main chip is damaged
N
Y
N
Y

## Slide 9
八、Function (HDMI, CVBS)
CI card is not recognized
Check whether the power supply
of the CI card is normal
Check external signal source
Check whether the main chip pin
signal is normal
Check the circuit between the terminal
and the main chip
main chip is damaged
N
Y
N
Y

## Slide 10
九. Function (CI)
CI
Check whether the terminal
power supply is normal
Check the 5V_M circuit
Check whether the DETECT
level is normal
Troubleshoot the DETECT circuit
main chip is damaged
N
Y
N
Y

## Slide 11
1. Power circuit diagram
AC
input
EMI
filter
Rectifie
AC/DC
Power convertor
92V/120V
output
Output
filter
Output
filter
92V/120V
output
12V
output
Feed
back
power amplifier、
The main IC、
Screen voltage
and so on
LED driver
LED
BL_ON
PWM_REF
PWM_DIM

## Slide 12
Check EMI open or L N short
Go to
check
Main
board
function
Check if
UB101 PIN2 Open
Check the power
components
damage or not
Check the rectifier
Check if output short
Check if RB101,
RB102 open
Non output, IR indicator light slake
Check if 12V output normal
Check if EB1 voltage
about √2Vac
Check if UB101PIN5
voltage is about 15V
Change damaged
components
Change short
components
Change damage resistors
Change UB101
2.Power Supply Trouble 1
N
Y
Y
Y
Y
Y
Y
Y
N
N
N
N
N

## Slide 13
Correct
the LED
cable
Check BL_ON&PWM_REF
Control signal
Check
Main
board
function
Change QB801/DB801
Check if LED output short/open
IR indicator light
up but backlight slake
Check if the LED output cable are
connected incorrectly or open
Check QB801/DB801
damage or not
Remove short/open status
Change UB801
3.Power supply for LED drive
Y
N
Y
Y
Y
Y
Y
N
N
N
Increase brightness/check if Sampling resistor is right
Y
check is part of the brightness is in dim status
check is all of the brightness is in dim status
Check if UB801 PIN 1 voltage is about 12V