## Slide 1
—Power supply
—Display
—Audio
—Function
TPD.NT72690.PB767 Trouble Shooting
TV Author : Xu Chengbin Checked By ：
POWER Author : Zeng Zhifeng Checked By ：

## Slide 2
1. Power circuit diagram
AC
input
EMI
filter
Rectifie
AC/DC
Power convertor
120V
output
Output
filter
Output
filter
120V
output
12V
output
Feed
back
power amplifier、
The main IC、
Screen voltage
and so on
LED driver
LED
BL_ON
PWM_REF
PWM_DIM

## Slide 3
Check EMI open or L N short
Go to
check
Main
board
function
Check if FB 1 Open
Check the power
components
damage or not
Check the rectifier
Check if output short
Check if RB101,
RB102,RB103 open
Non output, IR indicator light slake
Check if 12V、120V
output normal
Check if EB1 voltage
about √2Vac
Check if UB101PIN5
voltage is about 15V
Change damaged
components
Change short
components
Change damage resistors
Change UB101
2.Power Supply Trouble 1
N
Y
Y
Y
Y
Y
Y
Y
N
N
N
N
N

## Slide 4
Correct
the LED
cable
Check PWM_DIM&PWM_REF&
BL_ON Control signal
Check
Main
board
function
Change QB801/DB801
Check if LED output short/open
IR indicator light
up but backlight slake
Check if the LED output cable are
connected incorrectly or open
Check QB801/DB801
damage or not
Remove short/open status
Change UB801
3.Power supply for LED drive
Y
N
Y
Y
Y
Y
Y
N
N
N
Increase brightness/check if Sampling resistor is right
Y
check is part of the brightness is in dim status
check is all of the brightness is in dim status
Check if UB801 PIN 1 voltage is about 12V

## Slide 5
5. Power Troubleshooting
Check CNB2 for 12V
Check if the power
board is OK?
N
N
N
Check power on the TV board.
Repair or change
the power board.
Check UD4 for 5V ?
Check if the UD1/UD4
/U2 are damaged?
Check the CD42 for 2.5V.
2. Check the CD9 for 1.5V
Check the CD46 for 0.97V
Y
Y
Y
Change UD4?
N

## Slide 6
Indicator light on?
Check if power supply is ok (include 5V,1.0V,1.2 V,3.3V)
Check the output of UD2 for 3V3
Check CLK of YF1
Check if UE1 FLASH have upgraded or upgraded to death
Check UD2 power circuit
Check RK9 for 3V3?
Check YF1 or UE1 / FLASH
Check unmoral power supply module
N
N
Y
Y
Change main IC
U1
Y
N
N
N
Y
Y
Upgrade or change UE1 FLASH
Change IC
Change FLASH or YF1
N
Y
N
6. Display Troubleshooting (blank screen or show nothing)

## Slide 7
White screen
Check if the Panel cable is right and if well connected with the board
Check if G pole voltage of QW1 is low
Check if the panel is ok
Change the Panel cable
N
Y
Check if CW3 is 12V ?
Check power supply
Y
N
N
Y
Check the S pole of QW1 is 12V
Check if Panel connector jumper contact well
Change U1
Check if B pole of QW2 is high (0.6V) or front end of RW7 is 3.3V
N
Y
Change QW1
N
Y
Change QW2
Change Panel Connector or jumper
Change U1
Y
N
Change panel
7. Display Troubleshooting (white screen )
N
Y

## Slide 8
Picture display abnormal
Check if the VCC_Panel voltage is right ?
Check the LVDS cable is ok ?
Check if the circuit between the
LVDS jack and U1 are well soldered?
Change the LVDS cable
Change LCD
Y
N
N
Y
Y
Check U1 power supply and clock
Y
Repair this damage circuit
LCD is ok ?
N
Y
Upgrade software or adjust Panel setting
8. Display Troubleshooting (picture badness )
Y
Change U1

## Slide 9
No sound
Check if audio signal
Input is normal
Repair external
audio equipment
Check if the power of UA1 is OK?
Change the power
Check if the volume is rightly set or if mute function is off
Set it rightly
Check if the output signal on the Pin21/17 & Pin22/26 of UA1 is normal
Repair the speaker
Check if the audio signal input to UA1 is Ok
Check the audio circuit between the U1 and UA1.
Check if the UA1 is damaged?
N
Y
N
Y
N
Y
N
Y
N
Y
9. Audio Troubleshooting (no sound )

## Slide 10
TV can’t search channel, or no signal
external RF input
signal is ok ?
N
Check
external RF
equipment
Y
Check if the Pin 11/18/24 of UT2
is 3.3V
Check this
pin ‘s power
supply
Y
N
Check the pin 6/7 of UT2 I2C signal
Check I2C
network and
make sure
U1 is ok
Y
N
Check if the pin 15 voltage of UT1 is right ？
Check IF-AGC
Circuit
N
Y
Check if the pin 1/2 of UT1 has signal output ?
N
Check circuit
between UT2
and U1
Y
UT2 badness ,
change it
Change U1
N
10. Function Troubleshooting (TV fault)

## Slide 11
N
Y
PC/AV channel
sound is normal ？
Refer to “no sound ”
troubleshooting
Make sure input signal source is regular ?
N
Y
Signal source is not regular ,
check external equipment
EDID is right ？
N
Check HDMI periphery circuit or upgrade software
Y
Check if U1 is damage
11. Function Troubleshooting (HDMI no sound )

## Slide 12
N
N
Y
Y
Check if the HDMI cable is right
and if well connected with the board
HDMI periphery
circuit is ok ?
Repair welding or
change HDMI terminal
Correct abnormal
component
No signal or picture abnormal
change U1
12. Function Troubleshooting (HDMI no picture )

## Slide 13
N
Y
Check if the signal cable is right? and
single output equipment setup right?
Correct setup equipment ，
or change signal cable
Check the coupling circuit?
No signal
Repair the coupling circuit
Check circuit between input
terminal to U1，
And check software is ok
Change U1
N
Y
Y
13. Function Troubleshooting (CVBS no signal)

## Slide 14
14. Function Troubleshooting (other)
USB is abnormal
Repair the USB power